## Slide 1
A presentation on the project
Designing a 130 MW IGCC Power Plant with Carbon Capture
Md Tariful Islam 1502015
Mahbub Chowdhury 1502016
Suprio Kamal 1502026
MD. Shahriar Hossain 1502033
Dept. of Chemical Engineering
BUET

## Slide 2
Project Definition
Process Features
Geographical Data
Meteorological Data
Raw Material Specification
A Municipal Solid Waste (MSW) based Integrated gasification combined cycle (IGCC) power Plant having a capacity of 130MW alongside Carbon capture will be set up on the bank of Buriganga river, near the major dumping site of Dhaka..

## Slide 3
MSW is a low cost fuel
Compatible with gasification process.
Reduce landfill usage
Efficient Thermal conversion
Can become a carbon negative process
Low emission to environment
Offsets the use of fossil fuel
Features

## Slide 4
Raw Material Specification: MSW
Waste Type %Composition
Food waste 73.20
Wood 5.36
Paper 9.65
Cloth 8.57
Plastics 3.22
Chart: 
| Kitchen Waste | Wood | Paper | Cloth | Plastics
 | 0.73205 | 0.053591 | 0.096463 | 0.085745 | 0.032154

## Slide 5
Raw Material Specification: MSW
Proximate Analysis
Components %Composition
Ash 12.47
Volatile Carbon 75.83
Fixed Carbon 11.69
Chart: 
| Ash | Volatile | Fixed Carbon
 | 12.4722 | 75.8335 | 11.6932

## Slide 6
Raw Material Specification: MSW
Ultimate Analysis
Components %Composition
Carbon 47.61
Hydrogen 6.07
Oxygen 43.85
Nitrogen 2.19
Sulfur 0.28
Chart: 
| Carbon | Hydrogen | Oxygen | Nitrogen | Sulfur
 | 47.61 | 6.0726 | 43.8482 | 2.19 | 0.28

## Slide 7
Raw Material Specification: Coal
Proximate Analysis
Components %Composition
Ash 6.4
Volatile Carbon 48.46
Fixed Carbon 45.14
Chart: 
Chart: 
| Ash | Volatile | Fixed Carbon
 | 6.4 | 48.46 | 45.14

## Slide 8
Raw Material Specification: Coal
Ultimate Analysis
Components %Composition
Carbon 55.34
Hydrogen 5.07
Oxygen 24.7
Nitrogen 5.46
Sulfur 0.51
Chart: 
| Carbon | Hydrogen | Oxygen | Nitrogen | Sulfur
 | 74.61 | 5.13 | 10.69 | 8.72 | 0.85

## Slide 9
Component Mole fraction(%)
N2 68.20
H2O 16.31
O2 10.12
CO2 4.98
NO 0.33
CO 0.04
H2 0.02
CH4 0
Stack Gas Composition
Chart: 
| Nitrogen | H2O | Oxygen | CO2 | NO | CO | Hydrogen | Methane
 | 68.2 | 16.31 | 10.12 | 4.98 | 0.33 | 0.04 | 0.02 | 0

## Slide 10
Location : Geography
Notes: 141.8 Acre

## Slide 11
Location : Geography
Near the major dumping site for Dhaka
Flat terrain
Beside Buriganga, facilitating shipping
Almost 10 km
from Matuail

## Slide 12
Location : Meteorology
Temperature
Average Humidity
Wind Speed
Rainfall

## Slide 13
Location : Temperature
High temperature at April-September
Lowest at November-February
Max average yearly temperature = 35oC
Min average yearly temperature = 20oC

## Slide 14
Location : Average Humidity
Varies from 75% to 40%
Average at 60%
75%
50%
25%

## Slide 15
Location : Wind Speed

## Slide 16
Location : Rainfall
Average annual rainfall = 2148 mm
Maximum monthly rainfall = 373.1 mm
Average monthly rainfall = 179 mm

## Slide 17
Diameter:
Using Sherwood chart,
= 0.42
G2 = = 39
G = 6.23
AC = = = 1.58 m2
Diameter, D = =1.41m
Height
For D>0.55m, HETP=D0.3
HETP = 1.413 = 1.11 m = 49 inch
Again, HETP = K1
Height, Z = 7m
12% extra space is provided above the packing for necessary attachments
10% extra space required at the beneath of packing for liquid holdup
Design: CO2 Capture Stripper Column

## Slide 18
Thickness calculation
For temperature 103°C = 220°F
Operating fluid is MEA solution.
Carbon steel is chosen
Corrosion allowance ,C=3 mm
t = +C
Thickness, t= 1.14 inch
Vessel internals
Liquid distributor
Flash Plate Diameter = 3.64 ft
Number of holes required=
Hole diameter=0.5 in
Liquid Redistributor
For random packing Liquid redistributor is required at 3D distance interval
Number of liquid distributor =2
    Weight of the Tower Calculation
Maximum weight of tower, Wmax = Ws + WT + Wa
Where,
Ws= Shell Weight
WT = Weight of shell during water test
Wa =Weight of attachment
Wmax=55807 kg
Design: CO2 Capture Stripper Column

## Slide 19
Schematic: CO2 Capture Stripper Column

## Slide 20
P&ID: CO2 Capture Stripper Column

## Slide 21
Conventional Combustion Process
Feedstock is burned completely to produce steam
Electricity is produced through steam turbine
Integrated gasification and combined cycle(IGCC) process
Feed is gasified with shortage of oxygen
Impurities are removed before power generation cycle
Syngas produced is the fuel for gas turbine
Syngas cooler and gas turbine exhaust through HRSG make steam for the steam turbine cycle
Advantages of IGCC Process
Wide range of feedstock
Environment friendly and less pollution
  Easier carbon capture
  Dense pollutants easy to remove
  Less water needed
Higher efficiency
Process Selection

## Slide 22
Process Block Diagram
Feedstock Preparation

## Slide 23
Process Block Diagram
Overall Process

## Slide 24
Process Block Diagram
Raw Syngas Cleaning

## Slide 25
Process Flow Diagram

## Slide 26
Solvent : 70% MEA
Temp: 35o C
Pressure 2667 KPa
Material : Carbon Steel
Diameter Calculation:
Abscissa of Sherwood chart= = = 0.7333
Pressure Drop, ∆P = 0.115 Fp 0.7
Ordinate found to be 0.2
= 0.2
G(superficial mass flux) = 10.618 kg/m2s
G =
Ac =D2
D = 1.96m = 6.44 ft = 77.165 inch
Height Calculation:
D>.5m
HETP=D.3 =1.223m
McCabe Thiele Diagram
Number of stages= 6
Height of the packing = HETP N=7.338m
Height 8.0718m after overdesign(10%)
Total Height after extra space 9.847m=32.30ft
Design: CO2 Capture Absorber Column

## Slide 27: Shell Thickness
ASME Vessel code VIII
Thickness tS = +C=2.02 inch
Outer diameter: 77.32 + 2 = 81.3616 in
Column Internals
Liquid Distributor = Full cone spray nozzle
Flash plate dia=column dia=6.44ft
Liquid Re-distributor
Liquid redistributor needed at 3D distance
3D=19.32, packing height=24ft
Liquid redistributor needed= =1.24 1
Maximum weigh of tower
Wmax= Ws+Wt+Wa
Wa=WFlash plate +W liquid redistributor+ W Support plate
+metal hold down plate+ packing weight
Wmax=21.83 ton
Support of the tower:
Bracket system n=4 (4 brackets up to 3m diameter)
Wind load Pw= 0.5 ρaCpVa2
Compressive load =
P= = 6658 ton
Design: CO2 Capture Absorber Column

## Slide 28
Fig: Mechanical Drawing of absorber column
Fig: Schematic Diagram of absorber column
Schematic

## Slide 29
P&ID of CO2 Capture Absorber Column

## Slide 30
Equipment Name | Identification No. | Count
MSW Shredder | S101, | 4
Coal Grinder | G101, G102 | 3
Steam Kiln Dryer | D101, D102 | 2
Entrained Flow Gasifier | GR201 | 1
Quench Vessel | V201 | 1
Catalytic Desulphurizer | V301 | 1
Catalytic Regenerator | V302 | 1
Knockout Drums | V501, V502, V503 | 3
Syngas Cooler | HX201 | 1
Waste Heat Boiler | HX202, HX401 | 2
High Temperature Shift Reactor | HR401 | 1
CO2 Absorber | AB501 | 1
CO2 Stripper | SR501 | 1
Heat Recovery Steam Generation System | HS601 | 1
Gas Turbine | GT601 | 1
Steam Turbine (3 P) | ST602 | 1
List of Major Equipment
Equipment Name | Id No. | Count
O2 Compressor | C201 | 1
CO2 Compressor | C202 | 1
Air Compressor | C301 | 1
Equipment Name | Id No. | Count
Fresh Solvent Pump | P301 | 1
Rich Solvent Pump | P302 | 1
Lean Solvent Pump | P303 | 1

## Slide 31
Plot Plan

## Slide 32
Equipment layout

## Slide 33
General Schematic of Siemens SFG gasification island
Design: Entrained Flow Gasifier
Ref: Integrated Gasification Combined Cycle (IGCC) Technologies: Ting Wang, Gary Stiegel

## Slide 34
Sizing: Entrained Flow Gasifier

## Slide 35
Schematic: Entrained Flow Gasifier

## Slide 36
P&ID: Entrained Flow Gasifier

## Slide 37
FCI
Operational Cost
Depreciation (MACRS 7 years)
Tax
Revenue
Payback Period, IRR
Economic Analysis

## Slide 38
The plant is divided into 5 blocks
1. The Gasifier block:
Raw material treatment and gasification equipment
2. The Syngas Cleaning Block:
Desulfurizer and shift-reactors
3. The CO2 Absorption Block: Absorber Stripper
4. The Energy Block: Gas Turbine, Steam Turbine, Generators, Compressors
5. The Heat Recovery Steam Generator (HRSG): Network of Heat Exchangers
Purchased Equipment (PE) Cost = 30% of FCI. Find PE, Find FCI!
USD 41.1 million (2019)
USD 3.70 million (2019)
USD 570,000 (2019)
USD 17.8 million (2019)
USD 2.50 million (2019)
Total PE Cost = 65.6 million USD
So FCI = 218 million (USD)
Where Indirect Costs are 76.4 million USD (35% of FCI) and Direct Costs are 142 million USD Indirect Costs include Legal expenses, Engineering and supervision, construction expenses, Contingency
Direct costs include PE cost, installation costs, piping, instrumentation, electrical, buildings, auxiliary plants (WTP, storage etc), Land cost, service facilities, offsites.
Economic Analysis

## Slide 39
Economic Analysis

## Slide 40
Ref: Zoelle, A., Keairns, D., Turner, M. J., Woods, M., Kuehn, N., Shah, V., ... & Fout, T. (2015). Cost and Performance Baseline for Fossil Energy Plants Volume 1b: Bituminous Coal (IGCC) to Electricity Revision 2b–Year Dollar Update (No. DOE/NETL-2015/1727). NETL.
Operating Costs

## Slide 41
Revenue
Depreciation
Ref: Sullivan, W. G., Wicks, E. M., & Luxhoj, J. T. (2003). Engineering economy (Vol. 12). Upper Saddle River, NJ: Prentice Hall.
Cashflow, Revenue and Depreciation
PW (@10%) = $ 760M
IRR is 12.74%
Cashflow

## Slide 42
Gross Profit = Annual Revenue – (Depreciation + Annual Operating Costs)
Net Profit = Gross Profit – Tax
Net Annual Cash Flow = Net Profit + Depreciation
Payback Period
Chart: Years
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
PW of Cumulative Cashflow | -244203100 | -219150510.1651 | -204745849.1581 | -186428515.2099 | -166385362.5438 | -145969392.8499 | -127403815.3912 | -110531113.1648 | -93121681.9214 | -75416763.7019 | -59321383.5023 | -44689219.6845 | -31387252.5775 | -19294555.2074 | -8301193.9619 | 1692770.8068 | 10778193.3238 | 19037668.3392 | 26546281.9896 | 33372294.399 | 39577760.2258 | 45219092.7955
10% MARR Tax = 35 % on Gross Profit 21 year Project Life IRR is 12.74%

## Slide 43
Design: High Temperature Shift Reactor
CO+ H2O = CO2+ H2 , Exothermic
Is a heterogenous catalytic reaction where Fe2O3 is the catalyst promoted by Cr2O3 (chromia)
In an IGCC-CCS system, this reactor serves two purposes
Increase the CO2 partial pressure (Dry Basis) for efficient absorption.
Produce a cleaner syngas (low CO content) with higher H2 fraction.
Ref: 1. Rase, H. F., & HOLMES, J. R. (1977). Case studies and design data.
2. Rase, H. F. (1977). Chemical reactor design for process plants (Vol. 2). New York: Wiley.
3. Bednar, H. H., & Bednar, H. H. (1986). Pressure vessel design handbook.
4. Pis’mennyi, E., Polupan, G., Carvajal-Mariscal, I., Sanchez-Silva, F., & Pioro, I. (2016). Handbook for Transversely Finned Tube Heat Exchanger Design. Academic Press.

## Slide 44
Catalyst Requirement, How much catalyst do we need?
Flow Configuration, What’s the (minimum) mass flux?
Reactor Sizing, What’s the diameter & length of the reactor?
Insulation, What’s the thickness?
Wind & Earthquake loading, What’s the bending moment & shear force at the base?
Skirt Design, What’s the thickness & number of bolts?
Reactor Deadweight

## Slide 45
Catalyst Requirement : Determined by A finite element analysis.
W lb Catalyst
Inlet Conditions: Known
29 bar, 632 oF , -(i)-th step
Inlet moles and enthalpy known
4420 lbmol/hr CO
22100 lbmol/hr H2O
1055 lbmol/hr CO2
2890 lbmol/hr H2 214 lbmol/hr N2
T = 633 oF, 29 bar
Outlet moles unknown
Outlet specific enthalpy known
-(i+1) -th step
4 unknowns
1. Extent of reaction.
2. Heat of reaction (at temperature 632.5).
3. Reaction rate
(moles converted/lb catalyst)
4. Amount of catalyst, W.
4 equations!! – WE CAN SOLVE THIS!!
ΔHr = -11373 + 3.11 T – 0.0003 T2 + 1.89×105 T-1
- = ΔF × (-ΔHr)
-rCO = ψk( yCO yH2O – yCO2 yH2 / K) / (379 ρb)
Δw × (-rCO) = ΔF
Using eq 1 & 2, we can find heat of reaction ΔHr & extent of reaction ΔF After knowing outlet composition, we know, reaction rate –rco , knowing ΔF & –rco gives us W
Design: High Temperature Shift Reactor

## Slide 46
Keep repeating until temperature reaches 790 oF (catalyst deactivation temperature is 890 oF). If desired conversion is not reached cool it down and use a 2nd (and 3rd / 4th / 5th ) bed! And finally, using 5 beds, we got-
A 91.54 % conversion of CO.
Outlet temperature is 770 oF, Dry basis CO is 2.96%
1st bed mass = 22,450 lb conversion after 1st bed= 28.746%
2nd bed mass = 14,620 lb conversion after 2nd bed= 45.23%
3rd bed mass = 21,143 lb conversion after 3rd bed= 61.82%
4th bed mass = 36,711 lb conversion after 4th bed= 78.52%
5th bed mass = 80,223 lb conversion after 5th bed= 91.54%
Outlet flowrates FCO = 373.72 lbmol/hr FH2O = 18,049 lbmol/hr FCO2 = 5,100.9 lbmol/hr FH2 = 6,937.4 lbmol/hr FN2 = 213.97 lbmol/hr
Design: High Temperature Shift Reactor

## Slide 47
Diameter is chosen so the flux is above a minimum.
Minimum flux, G is determined by – 1. assuming a G value and seeing if qm is <0.3 oC.
2. iterate until A proper G is found.
*a Higher G results in a lower reactor size, but here our flowrate is fixed. Rm = Mm = Average molecular weight of the feed. (lb/ lb-mole) G = Mass flux of feed in the reactor (lb ft-2 hr-1) Rm = lb-moles of gas reacted per lb-moles of feed. Where am = the surface area of catalyst per unit mass of catalyst (sq ft/lb), Dp is dimension of the catalyst tablet (ft) ρp is particle density (lb/ cu ft) of the catalyst.
qm = Rm ΔHr = Heat of water-gas shift reaction (kJ/ lb-mole) Cpm = molar heat capacity of the feed gas, (kJ/ lb-mole/oC) qm = temperature gradient existing between the fluid phase and catalytic surface minimum G is = 1,400 (lb ft-2 hr-1), a diameter if 11 ft gives us a G of= 6,103 lb/hr/ft2
A height of 40 ft cylindrical vessel can accommodate the 5 catalyst beds with adequate spacing.
Skirt height 7.25 ft & Top elliptical head is 2.75 ft. TH = 50 ft.
Flow Configuration & Sizing

## Slide 48
Q = ; , kst = 40 W/m-K, , kin = 0.03 W/m-K,
hair = 30 W/m2-K
Assuming an insulation thickness and calculate the heat loss Q and outside temperature.
Heat loss through uninsulated vessel wall = 36.84 kW. Insulation thickness = 3 in. Heat loss through insulated vessel wall = 0.508 kW. Reduction in heat loss = 98.62% Vessel Insulation outer wall temperature = 39.89 oC
Reactor Operational Weight (including reacting fluid)
At the base, mass is 410,000 lb Considering- Reactor shell, head, insulation, ladder,
Ladder clips, support plate, fluid, catalyst, catalyst support, skirt shell, stiffening rings, thermowell, nozzles, finned tube radiator.
Wind velocity was 100 mph for moment at the base
The reactor is assumed to be a cantilever beam with distributed loadings for wind and earthquake loading calculations. The standard used was ASA A58.1-1955
Shear loads due to earthquake was 410 kips Seismic Moment at base was 2751.8 kips
Moment at base due to wind was 361040 lb-ft
Insulation

## Slide 49
Seismic Loading
Wind Loading

## Slide 50
Schematic: High Temperature Shift Reactor

## Slide 51
P&ID: High Temperature Shift Reactor

## Slide 52
Thank You